## Slide 1: Timer and Interrupt Mechanism
Lab 03

## Slide 2: Your work today
program 8051 to show some LED pattern like last week
but control using timer and interrupt mechanism

## Slide 3: Overview: program control using timer and interrupt

## Slide 4: Why use timer + interrupt
a program to do precisely timed control
Example: make LED switches precisely every 1 second
time
LED
LED
LED
LED
1 second

## Slide 5: Will you like to do it in this way?
How to set N?
  you need precise cycle count for each assembly instruction
time
LED
LED
LED
LED
1 second
while (1) {
  A = RR(A); //rotate right
  P0 = A;
  delay (N);
}
delay (int N)
{
int i;
for (i=0;i<N;i++);
}

## Slide 6: A better way to do timed control
use timer + interrupt
Example:
CPU
timer
counter
wake me up one second later
count for 1 second
Hey! Time-up!

## Slide 7: Basic concepts of interrupt mechanism

## Slide 8: What is an interrupt?
to “interrupt” the normal execution of a CPU
  turn to do something exceptional and then back to normal execution
  usually to serve external I/O devices

## Slide 9: Interrupt normal execution and then return
main()
{
while (…) {
…
//normal execution
…
}
}
keyboard_intr_handler ()
{
printf (“A”);
}
process ID. 1234
PC
$> press something
send interrupt
interrupt service routine (ISR)

## Slide 10: Timer + Interrupt for timed control
the conceptual idea

## Slide 11: A better way to do timed control
use timer + interrupt
Example:
time
LED
LED
LED
LED
1 second

## Slide 12: A better way: uses timer+interrupt
CPU
timer
counter
main () {
set_counter (100);
timer_go ();
…
//my own work
…
}
timer_intr_service ()
{
switch_LED ();
}

## Slide 13: A better way: uses timer+interrupt
CPU
timer
counter
main () {
set_counter (100);
timer_go ();
…
//my own work
…
}
timer_intr_service ()
{
switch_LED ();
}
wake me up 100 units of time later
Setup the timer and interrupt

## Slide 14: A better way: uses timer+interrupt
CPU does its own work and the timer go counting
CPU
timer
counter
main () {
set_counter (100);
timer_go ();
…
//my own work
…
}
timer_intr_service ()
{
switch_LED ();
}
100
99
98
…
1
0
time

## Slide 15: A better way: uses timer+interrupt
the timer sends an interrupt to CPU when time-up
CPU
timer
counter
main () {
set_counter (100);
timer_go ();
…
//my own work
…
}
timer_intr_service ()
{
switch_LED ();
}
100
99
98
…
1
0
time
wake up! (interrupt)

## Slide 16: A better way: uses timer+interrupt
CPU turn to the interrupt service routine
CPU
timer
counter
main () {
set_counter (100);
timer_go ();
…
//my own work
…
}
timer_intr_service ()
{
switch_LED ();
}
100
99
98
…
1
0
time
wake up!

## Slide 17: A better way: uses timer+interrupt
then back to its normal execution
CPU
timer
counter
main () {
set_counter (100);
timer_go ();
…
//my own work
…
}
timer_intr_service ()
{
switch_LED ();
}
100
99
98
…
1
0
time

## Slide 18: Summary
Interrupt mechanism:
  a hardware signal to inform CPU some event has happened
  makes CPU change its execution path
    turn to “Interrupt Service Routine” (ISR)
    then return to its normal execution path and status
Timer:
  an external counter to count up for specified time
  usually inform CPU with interrupt

## Slide 19: The 8051 part

## Slide 20: The 8051 architecture
You are playing this part today

## Slide 21: Imagination on 8051 architecture
Imagine how data flow in the architecture!
R0
R1
R2
…
R7
general purpose
registers
A
B
P0
…
…
special function
registers (SFR)
ALU
8051 CPU core
…
…
address
30h
31h
32h
internal memory

## Slide 22: Imagination on 8051 architecture
flow of an arithmetic instruction
R0
R1
R2
…
R7
general purpose
registers
A
B
P0
…
…
special function
registers (SFR)
ALU
8051 CPU core
…
…
address
30h
31h
32h
internal memory

## Slide 23: Imagination on 8051 architecture
data movement between memory and registers
the MOV instruction
R0
R1
R2
…
R7
general purpose
registers
A
B
P0
…
…
special function
registers (SFR)
ALU
8051 CPU core
…
…
address
30h
31h
32h
internal memory

## Slide 24: Imagination on 8051 architecture
the MOV also for registers
R0
R1
R2
…
R7
general purpose
registers
A
B
P0
…
…
special function
registers (SFR)
ALU
8051 CPU core
…
…
address
30h
31h
32h
internal memory

## Slide 25: Imagination on 8051 architecture
Imagine how data flow in the architecture!
R0
R1
R2
…
R7
general purpose
registers
A
B
P0
…
…
special function
registers (SFR)
ALU
8051 CPU core
…
…
address
30h
31h
32h
internal memory

## Slide 26: How to program the timer and interrupt mechanism on 8051

## Slide 27: Your program will look like this
main ()
{
TMOD = ???
TCON = ???
TH0 = ???
TL0 = ???
IE = ???
while (1); //infinite loop and do nothing
}
Timer_ISR ()
{
//change LED pattern
}

## Slide 28: Your program will look like this
main ()
{
TMOD = ???
TCON = ???
TH0 = ???
TL0 = ???
IE = ???
while (1); //infinite loop and do nothing
}
Timer_ISR ()
{
//change LED pattern
}
Fill in SFR registers to setup the timer and the interrupt

## Slide 29: Your program will look like this
main ()
{
TMOD = ???
TCON = ???
TH0 = ???
TL0 = ???
IE = ???
while (1); //infinite loop and do nothing
}
Timer_ISR ()
{
//change LED pattern
}
You don’t need to branch to control the LED pattern

## Slide 30: Your program will look like this
main ()
{
TMOD = ???
TCON = ???
TH0 = ???
TL0 = ???
IE = ???
while (1); //infinite loop and do nothing
}
Timer_ISR ()
{
//change LED pattern
}
The timer interrupt will be executed regularly once setup finished

## Slide 31: Things you need to know
main ()
{
TMOD = ???
TCON = ???
TH0 = ???
TL0 = ???
IE = ???
while (1); //infinite loop and do nothing
}
Timer_ISR ()
{
//change LED pattern
}
Where to place the timer ISR?
How to setup SFR registers for the timer and the interrupt?

## Slide 32: How to program 8051’s interrupt mechanism

## Slide 33: Things you need to know
How to set SFR registers
Where to place interrupt service routine (ISR)?
interrupt enable
registers to control the timer

## Slide 34: The IE register
imagine a path in the figure
set switches in the figure to enable the path
1
1
1
1

## Slide 35: Where’s the interrupt service routing?
IE0: 0x3 (external interrupt)
TF0: 0xb (timer 0 overflow)
TF1: 0x1b (timer 1 overflow)
RI, TI: 0x23 (for UART)

## Slide 36: So your program will looks like
org 0H
AJMP MAIN
org 0Bh
AJMP show_LED
…
MAIN:
…//your main program
show_LED: //the tmer interrupt service routine
MOV R0, #LED_pattern
MOV P0, R0
…
assembler directive: place my code from address 0x0b

## Slide 37: So your program will looks like
org 0H
AJMP MAIN
org 0Bh
AJMP show_LED
…
MAIN:
…//your main program
show_LED: //the tmer interrupt service routine
MOV R0, #LED_pattern
MOV P0, R0
…
timer 0 ISR starts from here

## Slide 38: How to program 8051 timer

## Slide 39: Overview of 8051 timer
two timers:
  timer 0: {TH0, TL0}
  timer 1: {TH1, TL1}
four modes (set by TMOD register)
  0: 13-bit mode
  1: 16-bit mode
  2: auto reload mode
  3: split mode

## Slide 40: The SFRs for counting

## Slide 41: Registers to control the timer mode
timer mode
timer mode

## Slide 42: How 8051 timer works
Step 1: set {TH, TL}=N
Step 2: enable counting by setup TMOD, TCON
Step 3: wait for timer overflow (check TCON)
TF=1 to indicate timer overflow
(0xffff reached)
1000
1001
1002
…
0xffff
0
time

## Slide 43: How to set lots of bits in TMOD, TCON, and IE
check these figures for the four timer modes

## Slide 44: Timer Mode 0

## Slide 45: Timer Mode 1

## Slide 46: Timer Mode 2

## Slide 47: Timer Mode 3

## Slide 48: Exercise: setup timer control registers

## Slide 49: In-Class Exercise
Suppose:
  one cycle period of the timer counter is 0.1ms
Q: How to program 8051 to send an interrupt every 1 second?

## Slide 50: The SFR setup
setup the counter
  count once every 0.1 ms
  count 10000 times for 1 second
  {TH0, TL0}=65536 – 10000 = 55536 = (1101100011110000)2
1
1
0
1
1
0
0
0
1
1
1
1
0
0
0
0

## Slide 51: The SFR setup
use timer 0 with mode 01
  mode 01: 16-bit timer
0
1
0
0
0
0

## Slide 52: The SFR setup
1
1
1
1
1
1

## Slide 53: Demo: make LED run using the timer interrupt

## Slide 54: Function of the demo
switches LED every 30 timer interrupts
time
LED
LED
a timer interrput
…
switches LED every 30 timer interrupts

## Slide 55: The demo program
org to force program address
and jump to actual ISR immediately

## Slide 56: The demo program
Infinite loop to send control signals to LEDs

## Slide 57: The demo program
The timer ISR
Change LED pattern every 4 times the ISR is executed

## Slide 58: The demo program
Setup the timer interrupt
Q: what is CKCON?

## Slide 59: The demo program
Setup port configuration

## Slide 60: Next Lab: Buttons

## Slide 61: Lab 04
Turning the LED pattern by buttons
8051
A
LED

## Slide 62: Lab04: the pre-lab report
(1) explain how to filter-out unstable signals when a button pressed
time
key_pressed
you pressed just once
but generate lots of pulses

## Slide 63: Lab 04: the Pre-Lab Report
(2) How to access a control register in memory-mapped I/O system with standard C programming?
  With address mapping of the I/O device given
  You have only standard C compiler and no special support for the underlying hardware