## Slide 1: Button control and De-Bounce Filter
Lab 04

## Slide 2: Your Task
Control the LED display by pressing a button
8051
A
LED

## Slide 3: Grading
Basic: each hit of the button moves up/down the LED (75%)
Bonus 1: (+15%)
  the LED runs automatically
  Hitting the button will change the pattern
  Hint: use timer interrupt to make two I/O devices work simultaneously

## Slide 4: Things you need to know for your task
How to program 8051 to receive an input signal from the button?
How to filter-out unstable signal when a button pressed?
  the de-bounce filter

## Slide 5: How to receive a button input

## Slide 6: How to detect the push button
A hit generates a logic 1 to an GPIO pin

## Slide 7: How to count number of hits to a button?
deal with unstable signal

## Slide 8: Things you need to know for your task
How to program 8051 to receive an input signal from the button?
How to filter-out unstable signal when a button pressed?
  the de-bounce filter
How to make 7-seg display and button controller work together?
  time-sharing scheme

## Slide 9: You may write such a program
count = 0;
while (1) {
  while (P1.3==0);
  //goto here if P1.3==1
  count++;
}
…
P1
CPU
core
8051 MCU
I/O device
0
prepare to receive input from an I/O device

## Slide 10: You may write such a program
count = 0;
while (1) {
  while (P1.3==0);
  //goto here if P1.3==1
  count++;
}
…
P1
CPU
core
8051 MCU
I/O device
1
Button pressed

## Slide 11: You may write such a program
What’s wrong with this program?
You think you just hit the button once but the CPU sense it for hundreds of times
time
clock
…
hit button once
button_hit
count = 0;
while (1) {
  while (P1.3==0);
  //goto here if P1.3==1
  count++;
}

## Slide 12: You may write such a program
What’s wrong with this program?
(2) Unstable signal when you pressed a button
time
key_pressed
you pressed just once
but generate lots of pulses
count = 0;
while (1) {
  while (P1.3==0);
  //goto here if P1.3==1
  count++;
}

## Slide 13: De-bounce filter
the design concepts

## Slide 14: Things you need to know for your task
How to program 8051 to receive an input signal from the button?
How to filter-out unstable signal when a button pressed?
  the de-bounce filter
How to make 7-seg display and button controller work together?
  time-sharing scheme

## Slide 15: How to filter-out multiple pulses from a press
time
key_pressed
you pressed just once
but generate lots of pulses
clock

## Slide 16: How to filter-out multiple pulses from a press
use a counter to count the time to stable
time
key_pressed
unstable
counter
0
N
N-1
N-2
…
1
0
key_input
0
unstable
N

## Slide 17: How to filter-out multiple pulses from a press
use a counter to count the time to stable
time
key_pressed
unstable
counter
0
N
N-1
N-2
…
1
0
key_input
0
unstable
N
keep counter=N when key_pressed = 1

## Slide 18: How to filter-out multiple pulses from a press
use a counter to count the time to stable
count-down to 0 when key released
time
key_pressed
unstable
counter
0
N
N-1
N-2
…
1
0
key_input
0
unstable
N

## Slide 19: How to filter-out multiple pulses from a press
use a counter to count the time to stable
time
key_pressed
unstable
counter
0
N
N-1
N-2
…
1
0
key_input
0
unstable
N
a one-cycle pulse for each key press

## Slide 20: De-Bounce Filter
How to program

## Slide 21: How to filter-out multiple pulses from a press
write a program for the hardware concept
time
key_pressed
unstable
counter
0
N
N-1
N-2
…
1
0
key_input
0
unstable
N

## Slide 22: De-Bounce filter programming
while (1) {
//Stage 1: wait for a button pressed
do {
key_hold = P0;
} while (!key_hold);
//Stage 2: wait for key released
key_release = 0;
count = N;
while (!key_release) {
key_hold = P0;
if (key_hold) {
count = N;
}
else {
count--;
if (count==0) key_release = 1;
}
}//Stage 2: wait for key released
//Stage 3:move LED pattern
LED_pattern = (LED_pattern << 1)+1;
if (LED_pattern=0xff) LED_pattern = 0xfe;
P1 = LED_pattern;
}//while (1)

## Slide 23: De-Bounce filter programming
wait for key pressed
while (1) {
//Stage 1: wait for a button pressed
do {
key_hold = P0;
} while (!key_hold);
//Stage 2: wait for key released
key_release = 0;
count = N;
while (!key_release) {
key_hold = P0;
if (key_hold) {
count = N;
}
else {
count--;
if (count==0) key_release = 1;
}
}//Stage 2: wait for key released
//Stage 3:move LED pattern
LED_pattern = (LED_pattern << 1)+1;
if (LED_pattern=0xff) LED_pattern = 0xfe;
P1 = LED_pattern;
}//while (1)

## Slide 24: De-Bounce filter programming
keep counter=N when key hold
start count-down when key_hold=0
while (1) {
//Stage 1: wait for a button pressed
do {
key_hold = P0;
} while (!key_hold);
//Stage 2: wait for key released
key_release = 0;
count = N;
while (!key_release) {
key_hold = P0;
if (key_hold) {
count = N;
}
else {
count--;
if (count==0) key_release = 1;
}
}//Stage 2: wait for key released
//Stage 3:move LED pattern
LED_pattern = (LED_pattern << 1)+1;
if (LED_pattern=0xff) LED_pattern = 0xfe;
P1 = LED_pattern;
}//while (1)
trying to figure out when a key is totally released

## Slide 25: De-Bounce filter programming
keep counter=N when key hold
start count-down when key_hold=0
while (1) {
//Stage 1: wait for a button pressed
do {
key_hold = P0;
} while (!key_hold);
//Stage 2: wait for key released
key_release = 0;
count = N;
while (!key_release) {
key_hold = P0;
if (key_hold) {
count = N;
}
else {
count--;
if (count==0) key_release = 1;
}
}//Stage 2: wait for key released
//Stage 3:move LED pattern
LED_pattern = (LED_pattern << 1)+1;
if (LED_pattern=0xff) LED_pattern = 0xfe;
P1 = LED_pattern;
}//while (1)
unstable counter value

## Slide 26: De-Bounce filter programming
keep counter=N when key hold
start count-down when key_hold=0
while (1) {
//Stage 1: wait for a button pressed
do {
key_hold = P0;
} while (!key_hold);
//Stage 2: wait for key released
key_release = 0;
count = N;
while (!key_release) {
key_hold = P0;
if (key_hold) {
count = N;
}
else {
count--;
if (count==0) key_release = 1;
}
}//Stage 2: wait for key released
//Stage 3:move LED pattern
LED_pattern = (LED_pattern << 1)+1;
if (LED_pattern=0xff) LED_pattern = 0xfe;
P1 = LED_pattern;
}//while (1)
count-down to 0 when a key is totally released

## Slide 27: How to make two I/O devices work simultaneously
About the bonus

## Slide 28: You may write such a program
while (1) {
  wait_button_pressed ();
  btn_count++;
  LED_display ();
}

## Slide 29: You may write such a program
do {
key_hold = P0;
} while (!key_hold);
//Stage 2: wait for key released
key_release = 0;
count = N;
while (!key_release) {
key_hold = P0;
if (key_hold) {
count = N;
}
else {
count--;
if (count==0) key_release = 1;
}
}//Stage 2: wait for key released
while (1) {
  wait_button_pressed ();
  btn_count++;
  LED_display ();
}

## Slide 30: You may write such a program
//scan for each digit
for (i=0;i<3;i++) {
P0 = pattern (digit[i]);
}
while (1) {
  wait_button_pressed ();
  btn_count++;
  LED_display ();
}

## Slide 31: You may write such a program
What’s wrong with this program?
do {
key_hold = ~P0;
} while (!key_hold);
//Stage 2: wait for key released
key_release = 0;
count = N;
while (!key_release) {
key_hold = ~P0;
if (key_hold) {
count = N;
}
else {
count--;
if (count==0) key_release = 1;
}
}//Stage 2: wait for key released
//scan for each digit
for (i=0;i<3;i++) {
P0 = pattern (digit[i]);
}
while (1) {
  wait_button_pressed ();
  btn_count++;
  LED_display ();
}

## Slide 32: You may write such a program
What’s wrong with this program?
You will never see button control and digit display work together
time
button
control
LED display
button
control
LED display
for seconds
for seconds
while (1) {
  wait_button_pressed ();
  btn_count++;
  LED_display ();
}

## Slide 33: Time-sharing to control multiple I/O devices

## Slide 34: The correct scheme
time-sharing to control all the I/O devices
LED
display
button
control
LED
display
button
control
LED
display
button
control
LED
display
button
control
switches in mini-seconds!
1 ms
0.1 ms
time

## Slide 35: A scheme for time sharing control
main program: for button control
timer ISR: to scan for digit display
infinite loop in the main program
triggered by timer interrupt
time
LED
display
button
control
LED
display
button
control
LED
display
button
control
LED
display
button
control
switches in mini-seconds!
1 ms
0.1 ms

## Slide 36: A scheme for time sharing control
LED
Display
button
control
LED
Display
button
control
LED
Display
button
control
LED
Display
button
control
1 ms
infinite loop in the main program
triggered by timer interrupt
main () {
….
while (1) {
//Stage 1: wait for a button pressed
do {
key_hold = P0;
} while (!key_hold);
//Stage 2: wait for key released
key_release = 0;
count = N;
while (!key_release) {
key_hold = P0;
if (key_hold) {
count = N;
}
else {
count--;
if (count==0) key_release = 1;
}
}//Stage 2: wait for key released
//Stage 3: increment button counter
button_count++;
}//while (1)
}
Timer_ISR () {
switch LED pattern;
}

## Slide 37: Appendix: Programming 8051 in C Language

## Slide 38: How to access a control register?
In memory-mapped I/O
Just access through a pointor
char *p;
p = (char*) 0x80;
*p = 0xaa;

## Slide 39: How to setup an interrupt service routine
use “interrupt” directive
The ISR table of Keil-C compiler: http://www.keil.com/support/man/docs/c51/c51_le_interruptfuncs.htm
Check demo LED_shift

## Slide 40: Coming up
Midterm project (TBA)
Lab 05: LCD Programming

## Slide 41: Lab 05: LCD Programming
Display “Hello World!” on the LCD

## Slide 42: Pre-Lab Question
Explain how to send a command/character to the LCD
  Show the timing waveform covering the following signals
    RS, RW, E, D [7:4]
Reference:
  http://www.8052.com/tutlcd.phtml
  http://www.eeherald.com/section/design-guide/sample_lcd_c_programs.html