## Slide 1: Graphics-LCD Display
Lab 06

## Slide 2: Your Task
Draw a still image on the graphics LCD
Bonus: show some animation

## Slide 3: Grading
Basic: (70%)
  “Draw” some still image
Optional: (animation)
  Move the pattern horizontally (+10%)
  Move the pattern vertically (+20%)
Report: (10%)
But this time you have to start from scratch
  No demo code for you to modify

## Slide 4: General Scheme to Control Graphics LCD
Fill the image bitmap into the display memory

## Slide 5: The control scheme
Fill-in the bitmap into the display memory
MCU
(8051)
Display Memory
(128x64 bitmap)
Graphics LCD
Driver
Screen
(128x64 pixels)
(address, data)

## Slide 6: Detailed look of the control scheme
Fill the 0-1 bitmap into two-dimensional array
But each time we fill 8-bit for 8 pixels on the x-axis
x
y

## Slide 7: Signal Interface to Fill the Image Memory
And the timing

## Slide 8: Signal Interface on Experiment Board
Through P2 and P4

## Slide 9: Signal interface to the LCD
RS: register select
  0: command
  1: data
RW: read/write select
  0: write
  1: read
E: latch enable
DB [7:0]
  the 8-bit data/command
CS1, CS2: select left/right half

## Slide 10: List of commands

## Slide 11: Timing diagram to send command/data
Notice the latch trigger on E
Has to check for busy

## Slide 12: Pseudo Code of the General Control Sequence
Convert each part to a sequence of accesses to ports P2 and P4
do {
read status;
} while (status==busy);
Set address x;
Set address y;
Write bitmap A;

## Slide 13: In-Class Exercise
Write a sequence of P2 and P4 value to reset and turn-on the graphics LCD

## Slide 14: In-Class Exercise
Write a sequence of P2 and P4 value to test whether the GLCD is busy or not

## Slide 15: In-Class Exercise
Write the series of P2 and P4 value to set a bitmap 0xAF on address x=3, y=25

## Slide 16: Pre-Lab Report

## Slide 17: Pre-Lab Questions
Q1: how to enable port P4 for input and output?
Q2: write a C function to set 8-bit bitmap on address (x, y)
  Draw (char x, char y, char bitmap)
Q3: find a tool to generate the bitmap of your image
  Please google!

## Slide 18: Suggestion: do this before you leave today
Use the SiliconLab IDE to manually draw some still image on the GLCD screen
  Key-in the value of P2 and P4 manually
  You have only sample code for basic setup