## Slide 1: General Purpose Digital I/O (GPIO)
Lab 02

## Slide 2: Objectives of this lab
to build up your imagination on how a program affects hardware signals
to learn how to send/receive signals from an application processor to external devices through I/O pads
I/O pins
to I/O devices
(e.g. LED)
from I/O devices
(e.g. keyboard)

## Slide 3: Your work today
design a LED box
  initial: all LED off
  the LED runs some pattern after some button pressed
    you can design your own pattern

## Slide 4: Outline
Basic concepts of I/O control
I/O model of legacy 8051 processor
SiliconLab C8051F040 I/O control
Simplified programming model

## Slide 5: Preparations before the Lab
Read the data sheet of SiliconLab C8051F040 SoC
  Chap. 17
Read the schematics of the Big8051 experiment board
  On LEDs

## Slide 6: Pre-Lab Report
Q1: Explain what is watch-dog timer
  Somewhere in your OS textbook
Q2: Explain what is memory-mapped I/O
  Check the textbooks of Computer Organization, Computer Architecture, or OS

## Slide 7: Pre-Lab Report (cont’d)
Q3:
  Read Figure 17.1 of C8051F040 spec and the schematics of Big8051
  List all control signal values to turn-on an LED at P0.0
Value of these
Control signals

## Slide 8: Pre-Lab Report (cont’d)
Q4:
  Read Figure 17.2 of C8051F040 spec
  List the values of all control registers to configure port P0 as a digital output port

## Slide 9: General I/O Control Model

## Slide 10: How a processor commands an I/O peripheral
Through access control registers
CPU
memory
disk
USB controller
GPIO
…
System interconnect
peripheral
Control register

## Slide 11: How a processor commands an I/O peripheral
Through access control registers
CPU
memory
disk
USB controller
GPIO
…
System interconnect
Command
Status

## Slide 12: How to access control registers: the memory-mapped I/O
Part of the addressing space is assigned to control registers
Each control register is mapped to some memory address

## Slide 13: How a processor commands an I/O peripheral
Through access control registers
CPU
memory
disk
USB controller
GPIO
…
System interconnect
Command
Status
0xd0
0xe0
mov 0xd0, #0101B
mov R1, 0xe0

## Slide 14: General Purpose Digital I/O
the processor assigns/examines the logical status of some I/O pins directly
CPU
core
0100101
P0
8051 chip
I/O pins
0100101

## Slide 15: I/O Model of Legacy 8051 Processor

## Slide 16: Features of 8051 I/O
four 8-bit I/O ports P0-P3
each pin is bidirectional
  sometimes input and sometimes output

## Slide 17: Features of 8051 I/O
four 8-bit I/O ports P0-P3
each pin is bidirectional
  sometimes input and sometimes output

## Slide 18: Features of 8051 I/O
four 8-bit I/O ports P0-P3
each pin is bidirectional
  sometimes input and sometimes output

## Slide 19: Features of 8051 I/O
four 8-bit I/O ports P0-P3
each pin is bidirectional
  sometimes input and sometimes output
I/O device
(e.g. keyboard)

## Slide 20: Features of 8051 I/O
four 8-bit I/O ports P0-P3
each pin is bidirectional
  sometimes input and sometimes output
I/O device
(e.g. LED)

## Slide 21: Imagination on 8051 architecture
Imagine how data flow in the architecture!
R0
R1
R2
…
R7
general purpose
registers
A
B
P0
…
…
special function
registers (SFR)
ALU
8051 CPU core
…
…
address
30h
31h
32h
internal memory

## Slide 22: How to program I/O ports?
through SFRs P0-P3

## Slide 23: How 8051 send out dedicated control signals
MOV R0, #01001101B
MOV P0, R0
CPU
core
0100101
P0
8051 chip
I/O pins
0100101

## Slide 24: The case of input (receive)
initial: set a bit (pin) with value 0
receive (input): wait for the bit to be toggled to be 1
P0.3 = 0
//wait unit P0.3 been set to 1
while (P0.3==0);
//action for the I/O event
…
P0
CPU
core
8051 MCU
I/O device
0
prepare to receive input from an I/O device

## Slide 25: The case of input (receive)
initial: set a bit (pin) with value 0
receive (input): wait for the bit to be toggled to be 1
P0.3 = 0
//wait unit P0.3 been set to 1
while (P0.3==0);
//action for the I/O event
…
P0
CPU
core
8051 MCU
I/O device
1
set to one to inform an event

## Slide 26: The GPIO of C8051F040 SoC

## Slide 27: Overview of SFR
Extension from legacy 8051
Divided into 3 pages
Page 145-149 of the C8051F040 data sheet

## Slide 28: The port configuration
Set XBR2, PxMDIN and PxMDOUT to set port Px as general purpose I/O

## Slide 29: The I/O pad
To send output 1
0
1
1
1

## Slide 30: The I/O pad
To send output 0
0
0
1
0

## Slide 31: Schematics of the LED
mov P0, #10000000h to turn on LD8

## Slide 32: Example 1
Detect button press and display on LED

## Slide 33: Example Code

## Slide 34: Example 2: wait for a button pressed

## Slide 35: Demo: wait for a button pressed
wait:
A = P1;
if (A==0) goto wait;
exit:
//something after button pressed
wait:
mov A, P1
JZ wait
exit:
//something after button pressed
…
P1
CPU
core
8051 MCU
I/O device
0
prepare to receive input from an I/O device

## Slide 36: Demo: wait for a button pressed
wait:
A = P1;
if (A==0) goto wait;
exit:
//something after button pressed
wait:
mov A, P1
JZ wait
exit:
//something after button pressed
…
P1
CPU
core
8051 MCU
I/O device
1
Receive signal from the button

## Slide 37: Example 3: make LED run
show how to output signal

## Slide 38: Demo: rotate the LED light
MAIN:
MOV A, #00000001B
MOV PSW, #00H
Loop:
MOV P0, A
LCALL Delay
RR A
LJMP Loop
MOV R0, #50
Delay: MOV R1, #40
Delay1: MOV R2, #249
Delay2: DJNZ R2, Delay2
DJNZ R1, Delay1
DJNZ R0, Delay
RET

## Slide 39: Demo: rotate the LED light
MAIN:
MOV A, #00000001B
MOV PSW, #00H
Loop:
MOV P0, A
LCALL Delay
RR A
LJMP Loop
MOV R0, #50
Delay: MOV R1, #40
Delay1: MOV R2, #249
Delay2: DJNZ R2, Delay2
DJNZ R1, Delay1
DJNZ R0, Delay
RET
control the LED through content of A

## Slide 40: Demo: rotate the LED light
MAIN:
MOV A, #00000001B
MOV PSW, #00H
Loop:
MOV P0, A
LCALL Delay
RR A
LJMP Loop
MOV R0, #50
Delay: MOV R1, #40
Delay1: MOV R2, #249
Delay2: DJNZ R2, Delay2
DJNZ R1, Delay1
DJNZ R0, Delay
RET
rotate right (RR) A
00000001
1000000
01000000

## Slide 41: Demo: rotate the LED light
MAIN:
MOV A, #00000001B
MOV PSW, #00H
Loop:
MOV P0, A
LCALL Delay
RR A
LJMP Loop
MOV R0, #50
Delay: MOV R1, #40
Delay1: MOV R2, #249
Delay2: DJNZ R2, Delay2
DJNZ R1, Delay1
DJNZ R0, Delay
RET
call a function at label “Delay”
a nested loop to delay some time

## Slide 42: The Next Lab: Timer and Interrupt

## Slide 43: Your Work at Lab 03
make LED run but using the timer interrupt to trigger pattern change

## Slide 44: Pre-Lab Report
Q1: what is interrupt?
  check Mano: logic and computer design fundamentals, Section 10-9
Q2: how to setup an ISR on 8051
  ISR: interrupt service routine